## Slide 1: Security camera System
EECE 381 Module 2 Presentation
Group2
Xu Chen, Peter Wang, Yuxin Xu, Michael Zheng

## Slide 2: Goals
Simple Security Camera App runs on Android devices
Security System App with sufficient features to function as a real Security System
Fully developed Security System App that people would be willing to pay for

## Slide 3: Description of our module
Our Security Camera System is capable of detecting any suspicious activity within the view of the camera.
An alarm will be triggered at the “security server” side and on the user’s mobile device if an activity is detected when the system is on.
While the alarm is on, real time photos taken by the camera will be transmitted to the server and to the user’s mobile device.
Photo reviewed at the server side will be saved on a storage device for further investigation.

## Slide 4: Interaction between each part
Security Camera App on Device A
Remote & Monitor App on Device B
Software on DE2
VGA Display
From Device B to Device A
On/Off instruction
From Device A to Device B
“Alarm Trigger” signal
Photos taken when Alarm is on
From Device A to DE2
“Alarm Trigger” signal
Photos taken when Alarm is on
From DE2 to VGA Display
Photos every interval of time when alarm is on
Notes: The whole module consist of 3 parts.
A Security Camera App runs on an Android Device
A Remote & Monitor App runs on another Android Device
A software that receives information from the Security Camera App, runs on a NIOS II system simulated on a DE2 board.

## Slide 5: Description of each part
Security Camera App on Device A
Takes a photo every interval of time
Remote & Monitor App on Device B
Listens for “Alarm Trigger” from Device A
Software on DE2
Listens for “Alarm Trigger” from Device A
Compares the new photo with the photo taken last time
Sends an “Alarm Trigger” signal to Device B and DE2 if any difference in photos is detected
When alarm is triggered, sends every taken photo to Device B and DE2
Receives and display photos from Device A
Receives and saves photos from Device A
Displays photos received on an VGA Display

## Slide 6: Major implementation on each part
Device A -- Camera
Communication with another Android Device via WiFi Direct
Communication with NIOS II on DE2 via Middle Man
Device B -- Remoter
Communication with Camera via WiFi
DE2 Board
Communication with Android Device via Middle Man
Saving photo on an SD card and display it on VGA Display
Picture comparing algorithm
Using camera to take photos continuously
Alarm Sound Effect

## Slide 7: Difficulties encountered
Implementation of Middle Man
  Crash for no reason no matter using USB or Serial
  Bitmap format configuration
Communication between Android devices
  Sync delay between the picture sent and picture received.
  Sending full sized bitmap is slow.
  Only able to communicate one way
Picture comparing algorithm
  Hard to determine whether alarm should be triggered just by evaluating the results of comparison.
  Two different comparison algorithms (Hash and Direct)
  Audio implementation (mp3 file choose)

## Slide 8: Current Status
Progress
Camera is working properly
Comparing algorithm provides satisfactory results
Possible Improvement Aftertime
Audio Implementation
DE2 Board and Android Devices Communication at a reasonable speed
Center supervisor
Remote control
Fancier UI

## Slide 9: Conclusion
  All goals in high-level design have been accomplished.
    Taking photos continuously
    Photo comparison
    Photo transfer
    Photo display at monitor and remoter
    Photo save and load